## Slide 1: Analysis of the energy sustainability of Machine Learning algorithms
Students:
Yin Jun
Tutors:
Prof. Meo Michela
Prof. Vallero Greta
23/10/2023
First presentation

## Slide 2: Step
1. Preliminary definition of scenarios of interest, KPIs, and case studies that will be used in the development of the energy assessment methodologies
2. Development of models for assessing the environmental impact of centralized AI algorithms
3. Development of models for the environmental impact of AI algorithms in distributed learning

## Slide 3: Step1
https://github.com/sovrasov/flops-counter.pytorch
 | Alexnet | VGG-11 | Resnet-18 | GoogLeNet
MACs | 940.95 M | 7.58 G | 1.75 G | 1.52 G
Number of Parameters | 46.76 M | 128.81 M | 11.18 M | 5.98 M
Average energy of each round | 34430.087 J | 113015.843 J | 112909.394 J | 124845.577 J
Average time of each round | 437.3 s | 1419.5 s | 1417.9 s | 1567.8 s
Average final reached train acc | 87.92% | 97.42% | 97.43% | 81.73%
Average final reached test acc | 87.99% | 89.31% | 89.85% | 81.88%
Dataset: FashionMnist
Original size: 1*28*28 pixels
Device: RTX3060(maximum power 80W)
Deep Learning Models:
MACs(Multiply-Accumulate Operations)
The unit for measuring the computational complexity of a deep learning model
The energy, time, final reached train acc and test acc results are the averaged valued of 10 rounds simulation
Get data through various simulations to build model for calculate power consumption

## Slide 4: Step1
https://github.com/sovrasov/flops-counter.pytorch
 | Alexnet | VGG-11 | Resnet-18 | GoogLeNet
MACs | 940.95 M | 7.58 G | 1.75 G | 1.52 G
Number of Parameters | 46.76 M | 128.81 M | 11.18 M | 5.98 M
Average energy of each round | 33635.658 J | 101025.244 J | 33225.415 J | 111809.926 J
Average time of each round | 180.7 s | 388.1 s | 174.6 s | 397.4 s
Average final reached train acc | 88.00% | 97.42% | 87.98% | 82.26%
Average final reached test acc | 88.23% | 89.07% | 88.04% | 81.46%
Dataset: FashionMnist
Original size: 1*28*28 pixels
Device: RTX4090(maximum power 450W)
Deep Learning Models:
MACs(Multiply-Accumulate Operations)
The unit for measuring the computational complexity of a deep learning model
The energy, time, final reached train acc and test acc results are the averaged valued of 10 rounds simulation
Get data through various simulations to build model for calculate power consumption

## Slide 5: Time consumption of each part of simulation(3060)
Alexnet
VGG-11
Resnet-18
GoogLeNet

## Slide 6: Time consumption of each part of simulation(4090)
Alexnet
VGG-11
Resnet-18
GoogLeNet

## Slide 7: Average time & energy consumption, train & test acc(3060)
Alexnet
VGG-11
Resnet-18
GoogLeNet

## Slide 8: Average time & energy consumption, train & test acc(4090)
Alexnet
VGG-11
Resnet-18
GoogLeNet

## Slide 9: Simulation result
For deep learning models, using synchronize can perfectly measure time consumption of each step during the training part.
All the data are using average values of 10 rounds simulation, with each round contains 10 epochs. And the average time consumption results of each epoch in different deep learning models are almost the same with a variation of less than 1 second.
During the training part, the two most time-consuming parts are the backward and the forward.
The MACs(Multiply-Accumulate Operations) can be used as a parameter to do the energy consumption prediction of a given deep learning model.
In the table presented in the first slide, the Resnet and VGG have better test accuracy than Alexnet about 2% but consume over 3 times the energy, which might be due to the dataset.
Using different GPUs can result significantly different running times, and some algorithms in different hardware may have significantly different energy consumption.
Next step:
Try to find more KPIs for building a model to calculate energy consumption
  Number of Parameters
  MACs
  Computational parallelism
  Hardware Utilization
  Communication Overhead

## Slide 10: Step
1. Preliminary definition of scenarios of interest, KPIs, and case studies that will be used in the development of the energy assessment methodologies
2. Development of models for assessing the environmental impact of centralized AI algorithms
3. Development of models for the environmental impact of AI algorithms in distributed learning

## Slide 11: Step2
PVWatts Hourly PV Performance Data |  | 
Requested Location | turin | 
Location | TORINO-CASELLE, ITALY | 
Latitude (DD) | 45.18 | 
Longitude (DD) | 7.65 | 
Elevation (m) | 282 | 
DC System Size (kW) | 14.2 | 
Module Type | Standard | 
Array Type | 2-Axis Tracking | 
Array Tilt (deg) | 0 | 
Array Azimuth (deg) | 180 | 
System Losses (%) | 14.08 | 
DC to AC Size Ratio | 1.2 | 
Inverter Efficiency (%) | 96 | 
Ground Coverage Ratio | NA | 
Albedo | From weather file | 
Bifacial | No (0) | 
Monthly Irradiance Loss (%) |  | 
 | Jan | 0
 | Feb | 0
 | Mar | 0
 | Apr | 0
 | May | 0
 | June | 0
 | July | 0
 | Aug | 0
 | Sept | 0
 | Oct | 0
 | Nov | 0
 | Dec | 0

## Slide 12: Step2
Preliminary set: energy consumption for training a model to a given accuracy is 10000kWh
Format of the hourly data
Format of the monthly data

## Slide 13: Thanks